Includes:

- Application charts for Gill and Concord aircraft battery

- Aircraft Battery cross references

- Gill aircraft battery specifications

- Concord battery specifications

- Computes battery state of charge for 12 or 24 volt aircraft and 12 volt automotive based on voltage, or specific gravity.

- Applies temperature correction.

- Compares self-discharge rates versus temperature for sealed and flooded batteries.

- Tells you how long the battery can sit before discharge and/or damage.

- Includes battery wiring diagrams.

- Aircraft Battery charging methods

- Battery connection testing

- Cannon and Elcon battery connectors

- Aircraft Battery definitions. AGM battery

Larger aircraft batteries use either a cannon battery connector or an elcon battery connector. Cannon is an older style.  Newer designs use an elcon connector.

Battery wiring diagrams. Batteries can be connected in parallel or series  or series-parallel.

Gill Aircraft Battery Specifications